# Class example: 152.77.0.0

Network ID = 152.77.0.0

default subnet mask = 255.255.0.0; 1111 1111.1111 1111.0000 0000.0000 0000

( 1 octet x 1 octet = 256 x 256 = 65,536 then – 1 bit = 32766 )

Remember always must subtract 2 for the all 0s and all 1s addresses (The first Subnet ID would be the zero subnet and the last would be the same id as the subnet mask of the subnetted octet just as the first Host address is all 0s and the last host address is all 1s)  unless your router supports RFC 1812 in which case you do not need to subtract the two from the NETWORK IDs – but you must still subtract the two from the HOST IDs!

| Subnet Mask | Subnet Mask | # of subnet IDs | # of host IDs |
| --- | --- | --- | --- |
| 1000 0000.00000000 | 128 | 2-2 =0 (invalid) | 32768-2=32766 |
| 1100 0000.00000000 | 192 | 4-2=2(too few network ids) | 16384-2 =16382 |
| 1110 0000.00000000 | 224 | 8-2=6 | 8192-2=8190 |
| 1111 0000.00000000 | 240 | 16-2=14 | 4096-2=4094 (too few host ids) |
| 1111 1000.00000000 | 248 | 32-2=30 | 2048-2=2046 |
| 1111 1100.00000000 | 252 | 64-2=62 | 1024-2=1022 |
| 1111 1110.00000000 | 254 | 128-2=126 | 512-2=510 |
| 1111 1111.00000000 | 255 | 256-2=254 | 256-2=254 |

1111 1111.1111 1111.1111 0000.0000 0000 = 255.255.240.0 =/20 =count the number of contiguous bits

1111 1111.1111 1111.1100 1000.0000 0000 = cannot be a subnet mask

# Determine the number of Subnet IDs

255.255.224.0 = 1111 1111.1111 1111.1110 0000.0000 0000

| 000 | 0 | 0 (invalid) |
| --- | --- | --- |
| 001 | 32 | 152.77.32.0 |
| 010 | 64 | 152.77.64.0 |
| 011 | 96 | 152.77.96.0 |
| 100 | 128 | 152.77.128.0 |
| 101 | 160 | 152.77.160.0 |
| 110 | 192 | 152.77.192.0 |
| 111 | 224 | 152.77.224.0 (invalid) |

# Easy Way

First ‘on’ bit from the furthest right is the first valid id then each is a multiple of the first i/e: 1110 0000= 32, then 32+32=64+32=96+32=128+32=160+32=192+32=224.

| Subnet mask | Subnet mask | 1st Subnet ID | Increment by |
| --- | --- | --- | --- |
| 1000 0000 | 128 | 128 | 128 |
| 1100 0000 | 192 | 64 | 64 |
| 1110 0000 | 224 | 32 | 32 |
| 1111 0000 | 240 | 16 | 16 |
| 1111 1000 | 248 | 8 | 8 |
| 1111 1100 | 252 | 4 | 4 |
| 1111 1110 | 254 | 2 | 2 |
| 1111 1111 | 255 | 1 | 1 |

I/e: 152.77.0.0 with a subnet mask of 255.255.248.0 = 152.77.8.0; 152.77.16.0; 152.77.24.0; etc.

with a mask of 255.255.255.0 = 152.77.1.0; 152.77.2.0; 152.77.3.0; etc.

33.0.0.0 with a subnet mask of 255.240.0.0 = 33.16.0.0; 33.32.0.0; 33.48.0.0; etc.

# Host ID in Binary

255.255.224.0 = 1111 1111.1111 1111.1110 0000.0000 0000

First Subnet ID is 152.77.32.0 = 1001 1000.0100 1101.0010 0000.0000 0000

First Host ID is 152.77.32.1 = 1001 1000.0100 1101.0010 0000.0000 0001

Second Host ID is 152.77.32.2 = 1001 1000.0100 1101.0010 0000.0000 0010

Third Host ID is 152.77.32.3 = 1001 1000.0100 1101.0010 0000.0000 0011

Last Host ID is 152.77.63.254 = 1001 1000.0100 1101.0011 1111.1111 1110

Second Subnet ID is 152.77.64.0 = 1001 1000.0100 1101.0100 0000.0000 0000

First Host ID is 152.77.64.1 = 1001 1000.0100 1101.0100 0000.0000 0001

Last Host ID is 152.77.95.254 = 1001 1000.0100 1101.0101 1111. 1111 1110

If you subnet the first Network ID=

152.77.0.0 subnet’s hosts run from 152.77.0.1 to 152.77.31.254

152.77.32.0 subnet’s hosts run from 152.77.32.1 to 152.63.254

152.77.64.0 subnet’s hosts run from 152.77.64.1 to 152.77.95.254

152.77.96.1  subnet’s hosts run from 152.77.96.1 to 152.77.127.254 and so on.

# REMEMBER! the hosts always run from .1 to .254

Subnet mask for all is 255.255.224.0

Now a Class C problem.

You have 210.77.10.0 network id

Default subnet mask of 255.255.255.0

You need 5 subnets which can support 25 hosts per subnet.

| Subnet Mask | Subnet Mask | # of subnet IDs | # of host IDs |
| --- | --- | --- | --- |
| 1000 0000 | 128 | 2-2 =0 (invalid) | 128-2=126 (invalid- all zeros) |
| 1100 0000 | 192 | 4-2=2(too few network ids) | 64-2=62 |
| 1110 0000 | 224 | 8-2=6 | 32-2=30 |
| 1111 0000 | 240 | 16-2=14 | 16-2=14 (too few hosts) |
| 1111 1000 | 248 | 32-2=30 | 8-2=6 |
| 1111 1100 | 252 | 64-2=62 | 4-2=2 |
| 1111 1110 | 254 | 128-2=126 | 2-2=0 (invalid) |
| 1111 1111 | 255 | 256-2=254 | 0 (invalid) |

# Remember – all hosts on the same physical segment share the same network id and subnet mask but must have a custom host id!

| 000 | 0 | 0 (invalid) |
| --- | --- | --- |
| 001 | 32 | 210.77.32.0 |
| 010 | 64 | 210.77.64.0 |
| 011 | 96 | 210.77.96.0 |
| 100 | 128 | 210.77.128.0 |
| 101 | 160 | 210.77.160.0 |
| 110 | 192 | 210.77.192.0 |
| 111 | 224 | 210.77.224.0 (invalid) |

Host IDs:

210.77.10.0 with 255.255.255.224

# Host ID in Binary 255.255.255.224 = 1111 1111.1111 1111.1111 1111.1110 0000

First Subnet ID is 210.77.10.32 = 1101 0010.0100 1101.0000 1010.0010 0000

First Host ID is 210.77.10.33 = 1101 0010.0100 1101.0000 1010.0010 0001

Second Host ID is 210.77.10.34 = 1101 0010.0100 1101.0000 1010.0010 0010

Third Host ID is 210.77.10.35 = 1101 0010.0100 1101.0000 1010.0010 0011

Last Host ID is 210.77.10.62 = 1101 0010.0100 1101.0000 1010.0011 1110

Second Subnet ID is 210.77.10.64 = 1101 0010.0100 1101.0000 1010.0100 0000

First Host ID is 210.77.10.65 = 1101 0010.0100 1101.0000 1010.0100 0001

Last Host ID is 210.77.10.94 = 1101 0010.0100 1101.0000 1010.0101 1110

| Subnet ID | 1st Host | Last host |
| --- | --- | --- |
| 210.77.10.0 invalid | 210.77.10.1 | 210.77.10.30 |
| 210.77.10.32 | 210.77.10.33 | 210.77.10.62 |
| 210.77.10.64 | 210.77.10.65 | 210.77.10.94 |
| 210.77.10.96 | 210.77.10.97 | 210.77.10.126 |
| 210.77.10.128 | 210.77.10.129 | 210.77.10.158 |
| 210.77.10.160 | 210.77.10.161 | 210.77.10.190 |
| 210.77.10.192 | 210.77.10.193 | 210.77.10.222 |
| 210.77.10.224 invalid | 210.77.10.225 | 210.77.10.254 |

Remember – no all 1s or all zeros. Stick to binary for class Cs—easier.

Subnetting more than one octet:

133.10.0.0 = class B

Default subnet mask of 255.255.0.0; we will subnet the last two octets

| Subnet Mask | Subnet Mask | # of subnet IDs | # of host IDs |
| --- | --- | --- | --- |
| 1111 1111.0000 0000 | 255.0 | 256-2=254 | 256-2=254 |
| 1111 1111.1000 0000 | 255.128 | 512-2=510 | 128-2=126 |
| 1111 1111.1100 0000 | 255.192 | 1024-2=1022 | 64-2=62 |
| 1111 1111.1110 0000 | 255.224 | 2048-2=2046 | 32-2=30 |
| 1111 1111.1111 0000 | 255.240 | 4096-2=4094 | 16-2=14 |
| 1111 1111.1111 1000 | 255.248 | 8192-2=8190 | 8-2=6 |
| 1111 1111.1111 1100 | 255.252 | 16384-2=16382 | 4-2=2 |
| 1111 1111.1111 1110 | 255.254 | invalid | 2-2=0 invalid |
| 1111 1111.1111 1111 | 255.255 | invalid | 0 invalid |

Classless – forget A, B, C etc.

classful was an inefficient use of IPs, and made for overuse of Internet routers. 232  = 4 billion addresses. imagine how many routes a router would need to know! Routers needed Router Aggregation (summation) to speed the process up.

ISP allocated an address of 206.10.0.0 subnet mask of 255.255.0.0

| Customer | One | Two | Three | Four | Five |
| --- | --- | --- | --- | --- | --- |
| needs # | 4000 | 2000 | 2000 | 4000 | 1000 |
| Subnet ID | 206.10.16.0 | 206.10.8.0 | 206.10.32.0 | 206.10.48.0 | 206.10.4.0 |
| Subnet mask | 255.255.240.0 | 255.255.248.0 | 255.255.248.0 | 255.255.240.0 | 255.255.252.0 |
| IP Address Range | 206.10.16.1 to 206.10.31.254 | 206.10.8.1 to 206.10.15.254 | 206.10.32.1 to 206.10.39.254 | 206.10.48.1 to 206.10.63.254 | 206.10.4.1 to 206.10.7.254 |

Customer 3 must go up by 8s; customer 4 must go up by 16s

How many needed? Figure out Subnet Mask needed without overlap.

Routing protocol must support Variable Subnet Masking.

Customer 2 is needing 2 subnets: 206.10.8.0, SNM of 255.255.248.0

| Subnet | One | Two |
| --- | --- | --- |
| needs # | 1000 | 1000 |
| Subnet ID | 206.10.8.0 | 206.10.12.0 |
| Subnet mask | 255.255.252.0 | 255.255.252.0 |
| IP Address Range | 206.10.8.1 to 206.10.11.254 | 206.10.12.1 to 206.10.15.254 |

They can only use allocated numbers, not 206.10.4.0!

Customer 4 also needs two subnets: 206.10.48.0, SNM of 255.255.240.0

| Subnet | One | Two |
| --- | --- | --- |
| needs # | 2000 | 2000 |
| Subnet ID | 206.10.48.0 | 206.10.56.0 |
| Subnet mask | 255.255.248.0 | 255.255.248.0 |
| IP Address Range | 206.10.48.1 to 206.10.55.254 | 206.10.56.1 to 206.10.63.254 |

To the Network Access Point (NAP) everyone would look like 206.10.0.0 with 255.255.0.0

Routing example:

A packet for 206.10.8.52 is at the NAP. The NAP looks at its routing table and sees that it should go to the ISP assigned that range of numbers. (it only looks at the first 2 octets as that is the masked part)

The router at the ISP receives the packet and looks at its routing table and sees that it belongs to the portion assigned to Customer 2 (it looks at the first three octets as it is masked).

Customer 2s router then receives the packet and forwards it to its final destination on subnet one.

Each router only needs to get the packet to the next router down the line.